## Slide 1: Federal Radiological Monitoring and Assessment Center Monitoring and Sampling Division Training
MS-50 Module 2
“Technical Field Team Training”
November 2020
U.S. Department of Energy
National Nuclear Security Administration
Nevada National Security Site
Notes: This course provides states/locals with an overview of FRMAC monitoring and sampling techniques during state outreaches.
There are 4 modules to this course. Module 1 contains a description of the FRMAC and the FRMAC Monitoring Division. Module 2 describes monitoring equipment and techniques. Module 3 describes sampling techniques from some common sample types. Module 4 describes some of the data and documentation needed for monitoring and sampling activities.
There is also a hands-on practical portion that to this course, if desired and weather permitting. The practical can cover basic monitoring techniques for exposure rate or contamination surveys as well sampling techniques for soil and air samples.

## Slide 2: MS-50 Module 2 Outline
Monitoring Equipment
Monitoring Techniques
Contamination Control
Notes: In module 2, we will discuss monitoring equipment, monitoring techniques, and basic contamination control.

## Slide 3: Monitoring Equipment

## Slide 4: Exposure Rate
Thin NaI
GM Tube
NaI Detector
Ion Chamber
Meter
Personal Radiation Detector
Notes: Exposure or dose rate instruments are one of the most common types of radiation detectors. These instruments come in a variety of shapes and sizes and can either contain an internal Geiger Mueller (GM) tube, scintillating crystal or material, or ion chamber. Typically, GM tubes are used in smaller, wearable type exposure rate detectors like a Personal Radiation Detector (PRD). Handheld exposure rate detectors may consist of a meter and a probe or may be combined into one unit. Generally, ion chambers are the most accurate measure of exposure or dose rate.

## Slide 5: Contamination Instruments & Probes
Alpha Beta Scintillator Probe
GM Pancake Probe
Removable Contamination
GM Pancake Probe
Notes: Contamination instruments measure radioactive contamination deposited on surfaces. Contamination instruments may consist of a meter and an attached probe, or may be combined into a single unit. Contamination probes are typically specialized in the type of radiation it detects. GM probes have the ability to generally detect alpha, beta, and gamma contamination. However, other probes, such as the sodium iodide probe, would be more sensitive to detecting gamma radiation than the GM. Alpha/beta scintillator probes are used to detect alpha and beta radiation only, with very minimal gamma radiation being detected. There are advantages/disadvantages to each probe. The most important thing to remember is to use a contamination probe that will detect the contamination of concern.

## Slide 6: Field Team Instrument Kit
Detectors
  Alpha, beta, and gamma probes
  Exposure/dose rate
  Alarming dosimeters
Uses
  Personnel surveys
  Dose measurement
  Contamination control
Notes: Field teams should have an instrument kit which contains various detectors. These instruments should be able to determine an exposure or dose rate and detect contamination (preferably be able to detect all types of radiation). There should be enough instrumentation for the field team to provide data for health and safety (personal dose or contamination control) and for performing environmental measurements for exposure or dose rates and ground deposition measurements.

## Slide 7: CMRT Health Physics Kit
First Plane - 12 Kits
Extra – 12 Kits
Notes: CMRT initially deploys with around 12 Health Physics Kits (HP Kits). The instruments provide the ability to perform dose rate measurements, detect alpha/beta contamination in the environment, and detect personal or equipment contamination. The kits consist of the following detectors:
Ludlum 9DP-1 Ion Chamber
Ludlum 3002 with 44-93 Alpha/Beta Scintillation Detector
Ludlum 26-1 Frisker
CMRT also has the same number of Ludlum 3001 with 44-2 NaI probes if the emergency necessitates the use of low energy gamma ray detection.
This is a good time for demonstration of the CMRT HPKIT or state/local equipment.

## Slide 8: LUDLUM 9DP-1 ION CHAMBER
Measures gamma Exposure
  Range: 200 µR to 50 R/hr
Low Pressure Ion Chamber
Auto-ranging & Zero
Notes: Ludlum 9DP-1 (ion chamber). These are used for dose rate measurements. Notice that the low range is 200 µR/hr which is well above the natural background exposure rate of around 10-35 µR/hr. For low range dose rate measurements, the Ludlum 3002 with a 44-2 scintillator or a Ludlum 26-1 with a dose filter (discussed later) may be used.

## Slide 9: LUDLUM 3002 with 44-93
Alpha / Beta Scintillation Probe
  Range: 0 cpm to 999 kcpm
Three modes of Operation
  RATE
  MAX
  COUNT
Notes: Ludlum 3002 (alpha/beta meter) connected to a 44-93 (alpha/beta scintillator). These are used for determining total alpha or total beta surface contamination. The common reporting unit is counts per minute (cpm) or kilo cpm (kcpm). Calibrating these instruments to a known source will determine a conversion coefficient to yield disintegrations per minute (dpm).

## Slide 10: LUDLUM 26-1 Frisker
Measures Beta Gamma Contamination
  Range: 0 cpm to 999 kcpm
  Range (with filter): 0 to 500 mR/h
Integrated Count
Three modes of Operation
  RATE
  MAX
  COUNT
Notes: Ludlum 26-1 (handheld GM). These are useful for frisking equipment and personnel for contamination and read out in cpm. The frisker can utilize a filter on the detector face to read out in exposure rate (mR/hr).

## Slide 11: LUDLUM 3001 with 44-2
Measures Beta Gamma radiation
  Range: 0 uR/hr to 49.9 mR/hr
  Range: 0 cpm to 999 kcpm
Low-level, wide-energy gamma detection
Modes of Operation
  RATE
  MAX
  COUNT
First Plane - 12 Kits
Extra – 12 Kits
Notes: Ludlum 3001 (meter) connected to a 44-2 (NaI detector). These are useful for surveying gamma emitters for either a contamination measurement (cpm) or as an exposure rate (µR/hr or mR/hr). These instruments would be useful in determining exposure rates near background levels or at levels below the minimum exposure rate of the 9DP-1 (<200 µR/hr).

## Slide 12: High-Purity Germanium (in situ) Detector
Uses
  Radioisotope identification
  Activity quantification
  Low level detection
Detectors
  High purity germanium
  Gamma only
  Mechanically cooled detector
    requires 12-24 hours to cool down
First Plane 2 - Ortec Detective DX
Extra – 3 Ortec Detectives
Notes: The Ortec Detective is a mechanically cooled high purity germanium (HPGe) detector. This detector sits on a tripod 1 meter above the ground. The Ortec Detective is what CMRT uses for in situ ground deposition measurements. HPGe detectors are used to identify specific radionuclides and quantify the activity of those radionuclides. Generally, HPGe detectors should be used in areas where the exposure rate is < 5 mR/hr to reduce the dead time of the detector.

## Slide 13: Radiation Monitors – Pressurized Ion Chamber
True and Accurate Dose Measurements
Aerial Measurement Support:
  Normalize Aerial data to Dose Measured @ 1 meter
  Trending changes over time
  Portable
3 GE RSDetect
Notes: As mentioned before, handheld ion chambers are used for exposure or dose rate surveys. CMRT also uses other ion chambers to support aerial measuring systems with their ground measurement calibrations. These ion chambers are more sensitive than the handheld ion chambers, can measure environmental background radiation doses, and are mounted on tripods.

## Slide 14: Search Instruments
Can characterize the extent of deposition (in low dose rate areas)
Can be used as impromptu portal monitors
Notes: Traditionally, search instruments have only been used for searching for illicit sources of radioactive material. However, these detectors can be used to support a Consequence Management response. Car borne and backpack systems can be used to characterize the extent of deposition. The limitation would be that these systems would be saturated and not work in areas with dose rates higher than 5-10 mR/hr. These detectors could also be used as impromptu portal monitors to survey equipment and people.

## Slide 15: FIDLER - Field Instrument for Detecting Low Energy Radiation
Used to detect alpha emitters via gamma radiation.
Single channel analyzer count rate meter
Preset region of interest for
17 keV or 60 keV
Display Counts per
Second
Notes: FIDLERS are generally used to detect alpha emitters by the x ray and gamma radiation emitted by the same isotope. These detectors are a sodium iodide crystal which is paired with a survey meter. They are easy to operate, but not very common outside the DOD or DOE. FIDLERs were designed to measure ground contamination for a dispersion of plutonium from a radioisotope thermoelectric generator (RTG) or nuclear weapons accidents. During the calibration process, the detector is calibrated to either the 17 or 60 keV energy. The survey meter displays counts per second or counts per minute. One would need a calibration factor to convert from a count rate to a surface contamination unit (Bq/m2).

## Slide 16: SpecFIDLER – Spectral Field Instrument for Detecting Low Energy Radiation
Measure ground contamination for plutonium dispersal from Radioisotope thermoelectric generator (RTG) or nuclear weapons accidents
Thin crystal Sodium Iodine (NaI) scintillation detectors
Americium-241 and Plutonium Low-Energy X- and gamma rays
20 - SpecFIDLER
Notes: CMRT uses the SpecFIDLER which utilizes the FIDLER detector but has a custom electronics package with an multi-channel analyzer which produces a spectrum. The unit has the ability to work as a traditional FIDLER with a count rate displayed or estimate the surface contamination value for the radionuclide of interest in Bq/m2. CMRT will deploy with SpecFIDLERs as needed by the incident type.

## Slide 17: FIDLER vs. Alpha Probe
FIDLER
Good when wet
Less sensitivity
Awkward to carry
Bigger Probe
More durable
Cover survey area faster
Alpha Probe
  Water (rain or dew) affects response
  Better sensitivity
  Easier to carry
  More susceptible to contaminating the detector
Notes: FIDLERs are preferable over alpha probes if durability and weather are an issue. Alpha probes are more sensitive and easier to carry.

## Slide 18: Air Sampler
Types
  High volume air flow
  Low volume air flow
  Particulate filters
AC or DC powered
Uses
  Detect airborne contamination
  Monitor re-suspension
  Personnel protection
Low and high volume for measuring airborne contamination
Notes: Air samples are useful in determining radionuclide concentrations present in the air during a release. Air samples are also useful in determining the resuspension rate of ground contamination (after the release has stopped). High volume air samplers are used for grab samples (lots of air in a short amount of time) during field team operations and releases. High volume air samplers require a power source. Low volume air samplers have an air flow similar to the human breathing rate and the air samples are usually collected for many hour or days. Low volume air samplers can run with a battery.

## Slide 19: Air Sample Pump
First Plane
  5 - High Volume samplers with 4-inch paper
  5 - low volume samplers with either 2-inch filter paper alone or charcoal cartridge
Extra
  19 - High Volume samplers with 4-inch paper
  14- low volume samplers with either 2-inch filter paper alone or charcoal cartridge
Notes: CMRT arrives with a mix of high and low volume air samplers. More air samplers are available, but may not be on the first plane out to the incident site. CMRT will deploy with air filters (4 inch air filters for the high volume air samplers and 2 inch air filters for the low volume samplers). CMRT will also bring charcoal cartridges for the low volume air samplers.

## Slide 20: Dosimeters
EPD (Electronic Personal Dosimeters)
Passive Dosimeters
MIRION DMC 3000
First Plane – 50
Extra - 69
  Panasonic UD802
  First Plane - 250
  Extra – TLD’s supplied from NNSS
Notes: Dosimeters are issued to all the Field Team Members. Thermoluminescent Dosimeters (TLDs) are counted and the results are recorded using a National Voluntary Laboratory Accreditation Program (NVLAP) accredited laboratory. CMRT/FRMAC uses the management and operating contractor at the Nevada National Security Site to process dosimetry. TLDs are being phased out by CMRT in favor for optically stimulated luminescence (OSL) dosimeters.

## Slide 21: Personal Protective Equipment
Clothing
  Protective coveralls
  Full Face Respirator
  Gloves
  Booties
One time use
Disposable
Uses
  Personnel protection
  Contamination control
  Radiation safety
Used to protect personnel from contamination
Notes: CMRT’s first plane will carry PPE. CMRT strives to have enough PPE for 5 Field Teams and Hot Line Support for 7 Days until a resupply would be necessary. PPE requirements will be made by the Health and Safety officer of the event. PPE requirements are expected to vary according to location. Some places may require a full set of PPE while other locations may require only booties and gloves.

## Slide 22: Monitoring Techniques

## Slide 23: Monitoring Techniques
General Cautions and Guidance
Deposition Characterization Survey Planning
Survey Types

## Slide 24: Survey Precautions
Do not put yourself in danger
All monitoring activities should follow As Low As Reasonably Achievable (ALARA)
Follow Turn-Back Levels
Try to avoid re-suspending contamination
Notes: The next few slides are general precautions that should be taken before and during field team deployments.
Field team activities are planned with safety in mind, however the unexpected could occur. No survey is worth your personal safety. Be aware of your surroundings (wildlife, dangerous crowds, bad weather, etc.). Be aware of the radiological hazards and follow established turn back levels or hold points. Avoid kicking up dust while working to decrease the internal dose hazard.

## Slide 25: Driving Precautions
Observe the ambient dose rate using the most sensitive instrument and scale to provide the first radiation measurements:
Hold the survey meter inside the vehicle and above the lap
Keep vehicle windows closed, vents on re-circulate
Upon observing ambient dose rate reach turn-back levels, notify Supervisor of your location and reading
Notes: Field teams will spend a good amount of time in vehicles. Be mindful of traffic and all local laws. The driver’s job is to drive only. Others in the vehicle can watch the meter, record data, and give directions. While in the vehicle, be aware of the exposure rate when entering the impacted area. Observe turn back levels at all times.

## Slide 26: Data Recording
Best to have instruments set up in RadResponder (or other system) BEFORE something occurs
Record all required data fields
Record the value and units displayed on the instrument (raw data)
Have a paper log as a backup
Notes: Setting up your instruments in RadResponder (or other system) before an incident occurs will ease the burden on the data collector. Efficiencies for unit conversions can be inputted into RadResponder (or other system) so the data collector only needs to report the raw value and unit. The conversion to a standard unit can be done by data assessors. Ensure that the survey is recorded (either electronically or on a paper survey log) and that the required fields are completed.

## Slide 27: Initial Monitoring
Monitor for everything
  Alpha
  Beta
  Gamma
Identify the isotopic mix of the deposition
Once the radionuclide(s) are identified, adjust techniques or frequency
Notes: It is important to survey for all types of radiation when initially responding to an unknown radiological hazard (example: if responding to a radiological dispersal device). As First Responders arrive at the incident, they may not have a lot of experience with radioactive material and have limited equipment and knowledge. Gamma exposure rate is generally the first survey completed. Sometimes it may be the only survey that may be completed due to lack of instrumentation. However, gamma exposure rate surveys will not detect all the types of radiation or contamination. Alpha/beta surface contamination surveys and air sampling may not be completed by first responders due to lack of time, equipment, or training. Alpha radiation is easy to miss unless you are looking for it with the right detector. Generally, for a consequence management response, neutron surveys are not performed.

## Slide 28: Monitoring Techniques
General Cautions and Guidance
Deposition Characterization Survey Planning
Survey Types

## Slide 29: Deposition Characterization
One major objective of the Monitoring Division is to determine the extent of the contamination and establish area boundaries.
  What is the extent?
  How wide is the area?
Some basic survey patterns of use:
  10 Point Monitoring Survey
  Boundary Survey (without entry)
  Transect Surveys
Notes: After a release, characterizing the extent of the deposition is a crucial task. For the initial response, typically only field teams are available to take measurements. A survey pattern should balance the time it takes to collect measurements and the relative value of the data collected to help inform protective action decisions. We will discuss 3 survey techniques that address initial monitoring: the 10 Point Survey, Boundary Surveys, and Transect Surveys.
Fully characterizing an area after a major release (like a nuclear power plant accident) could take weeks of surveying and will most likely necessitate assistance from federal assets like Aerial Measuring Systems to fully characterize large areas.

## Slide 30: 10 Point Monitoring Survey
Standardized methodology for quickly gathering required radiological monitoring information.
Identify ground deposition, plume direction, and source term.
Identify the extent of boundary of the contamination
Collect exposure rate, contamination readings, and either a soil sample or in-situ measurement. This will help with isotope identification and quantification.
Number and spacing between the points depend on:
  Number of responders
  Size of affected area
Notes: The Ten-Point Monitoring Strategy is a standardized methodology for quickly gathering required radiological monitoring information after a potential release. The strategy is intended to be used during the early post-incident phase (typically completed by the RAP team or first responders). The goal of this survey is to determine the downwind extent of the release (length and width) by providing 10 points in strategic locations. This strategy will allow a quick comparison of real-world data to model predictions and allow responding personnel to provide effective recommendations on protection of responders and the local population. The strategy is intended for use during the initial response and is not intended to guide selection of monitoring activities for follow on cleanup and site restoration tasks.

## Slide 31: Boundary Surveys
Use model to approximate boundaries
Perform a boundary survey:
  Identify boundaries without entering area
  Identify boundaries by transecting the area.
Notes: Another method to define ground deposition is to do a boundary survey. The boundary survey could occur in the following ways:
1.) Define a boundary without further entering the deposition area or
2.) Define the boundary by transecting the deposition area.

## Slide 32: Boundary Survey without Entry
Start at low background
Stop at a predetermined dose rate
Retrace route
Proceed laterally and repeat
Notify base at pre-set levels
Notes: The purpose of this survey is to identify area boundaries within which exposure rates and/or contamination levels exceed the derived response levels for evacuation/shelter-in-place, relocation, or other limit. Start recording data at a low background and work towards the deposition footprint. When the contamination level is approached, then move away laterally away from the footprint (as in the picture). Record measurements and (if needed) notify supervisor of your location and reading. Performing boundary surveys in this manner will cause field teams to avoid the greatest amount of dose and contamination by not traversing through the middle of the deposition footprint.

## Slide 33: Transect Surveys
Use model to approximate the boundaries
Decide if transects are worth the dose
  Risk vs. benefit
  ALARA
Start at a low background area
Collect measurements at a set interval
Notes: This pattern is used to define the deposition boundary by traversing through the area.
Some benefits of doing this pattern:
May be quicker performing this survey than performing a boundary survey without entry into the area.
Able to collect measurements and samples in the center of the deposition area (good for refining the model)
Collecting measurements and samples within the area will provide insight for the affected neighborhoods/towns.
Some cons to this pattern:
Subject teams to higher dose rates and/or contamination levels.
More risk of contaminating personnel/equipment.

## Slide 34: Transecting the Ground Deposition
Collect readings at set intervals
Continue survey until readings return to starting levels
Proceed laterally and repeat
Notify base at pre-set levels
  Example: 10 times background ~(100 μRem/h) or exposure rate increases of 1 mrem/h
Observe turn back levels
Notes: The purpose of this survey is to identify area boundaries within which exposure rates and/or contamination levels exceed the derived response levels for evacuation/shelter-in-place, relocation, or other limit. Start recording data at a low background and work towards the deposition footprint. Collect measurements at a specified interval during the transect. Continue surveying within the footprint until the levels decrease. Then repeat the transect (as in the picture). Record measurements and (if needed) notify supervisor of your location and reading. Be aware of established turn back levels.

## Slide 35: Monitoring Techniques
General Cautions and Guidance
Deposition Characterization Survey Planning
Early Phase Survey Types

## Slide 36: Evolution of a Response
Early Phase (Duration Hours to Weeks)
  Focuses on quick results for immediate protective action decisions
    Worker protection
    Public shelter / evacuation
Intermediate Phase (Duration Weeks to Months)
  Focuses on Derived Response Levels (DRL)
    Re-entry decisions
    Examining crop embargo areas
Late Phase (Duration Months to Years)
  Focuses on environmental / clean-up levels
Measurements and samples will focus on supporting these decisions
Notes: Radiological emergencies are typically broken into 3 phases. In the USA, the 3 phases of a radiological emergency are named Early, Intermediate, and Late. The international community will call these 3 phases Urgent, Early, and Recovery. Different phases of the response will dictate different measurements and samples.
During the Early Phase (sometimes referred to as the Emergency or Plume Phase), material is still being released into the environment. The duration of this phase is hours to days. For reference, Fukushima’s Early Phase lasted for 2 weeks.
The Intermediate Phase starts when the release has stopped and for several weeks or months afterwards. During this phase, it is time to determine the full extent of the impacted areas.
The Late (sometimes referred to as the Recovery phase) begins after the intermediate phase and lasts for months to years. Full characterization and clean up occur during this phase. EPA would be in charge of the FRMAC at this stage.

## Slide 37: Early Phase - Types of Surveys
Plume Survey
  airborne radioactive material
Ground Deposition
  exposure rate
  contamination
Public Support
  infrastructure
  evacuation / reentry
Notes: During the early phase, the most prevalent surveys will be exposure rate and contamination surveys. Exposure rates should be taken at 1 meter (waist height) above ground level. Contamination surveys (alpha/beta/gamma) are performed at ground level. Plume tracking surveys could also be performed by field teams or one could use a system of pre-existing fixed monitors to track the plume. Other surveys performed may be in support of maintaining critical infrastructure or public health which require surveying areas, people, and/or equipment.

## Slide 38: Plume Tracking
Surveys are used to identify:
  Inhalation exposure from the plume
  External exposure from the plume
  Absorption due to contamination of skin and clothes
Types of surveys:
  Air Samples
  Portable instrument looking at the ratio of:
    Gamma & beta/gamma and
    Between exposure rate (1 meter) and ground (3 cm) measurements
Notes: Conduct plume tracking surveys by measuring ambient dose rates in order to determine if a) the PAG (Protective Action Guides) are exceeded and if b) the turn back guidance for emergency workers is to be applied. Conduct further plume traverse/tracking as directed by the supervisor. Because this survey possibly subjects field teams to being immersed in a radiological plume, appropriate PPE with respirators and electronic dosimeters may be required. When driving in and around the plume, remember the basic safety precautions aforementioned. Personal safety, applicable PPE, and protective measures should be covered during a pre-deployment brief.

## Slide 39: Open Window / Closed Window Technique
By comparing readings to the table below determine if the plume is elevated, at ground level or has passed.
WO - window open; WC - window closed
If at waist level: WO WC | AND | If at ground level: WO WC | Then:
Β+ ≈  | AND | Β+ ≈  | Plume is elevated
Β+ >  | AND | Β+ >  | Plume is at ground level
Β+ ≈  | AND | Β+ >  | Plume has passed - ground contamination
This only works for Beta and Gamma measurements
Notes: To perform this technique, a beta/gamma probe with a window for taking open (β+y) and closed (y) readings must be used.
Perform a radiological survey at waist level (approximately 1 m above ground) and at ground level (approximately 3 cm above ground) with the detector looking toward the ground.

## Slide 40: Ground Deposition Measurements
Survey area should be:
  Undisturbed, relatively level
  Open area, away from trees, heavy traffic areas, buildings
  If possible, perform surveys at least 3 meters (10 feet) to the side of the road.
Alpha/beta contamination surveys (taken at ground level)
Exposure rate (taken at 1 meter above ground)
In situ measurements (taken at 1 meter above ground)
Notes: Ground deposition measurements are collected to determine the levels of contamination on the ground surface. Use contamination meters and in situ detectors to determine ground deposition. These measurements are common throughout the whole response. Find an open area that is undisturbed to take measurements. Contamination surveys are performed at ground level. In situ measurements are also performed at 1 meter above ground level (or however your system is calibrated). Typically, ground deposition surveys are always accompanied by an exposure rate survey performed at 1 meter above ground level (waist height).

## Slide 41: Ground Deposition Practical
Exposure Rate
  1 meter above ground level and ground level
Surface Contamination
  Typically at ground level
    Alpha
    Beta – beta/gamma
    Fixed + Removable
Isotopic Identification – In situ
Notes: Activity: Use instruments to perform an exposure rate survey at 1 meter and a surface contamination survey. If an in situ detector is available, practice collecting a spectrum.

## Slide 42: Transportation Corridors
Transportation Corridors
  Surveys are used to evaluate the contamination levels of a road
  Local governments use this information for evacuation and reentry planning
For covering a large area
  Use aerial equipment where available
  Drive the roads with a vehicle- mounted system
Notes: For covering a large area it is recommended to make measurement from within a moving vehicle (route monitoring) or to use aerial survey.
Ground deposition surveys on a roadway are used to survey and evaluate the contamination levels of a road. Local governments use this information for evacuation and reentry.

## Slide 43: Transportation Corridors
Notes: One could use a vehicle mounted search system to survey transportation corridors. For sodium iodide systems, surveys could be performed in areas that are less than 5-10 mR/hr (or whatever the sensitivity of the system may be). This slide is an example of transportation surveys in Japan.

## Slide 44: Habitability, Infrastructure, and Re-Entry
Critical or Sensitive Facilities
  Hospitals
  Areas under shelter orders
  Transportation hubs
  Power Plants
  Communication Switching Stations
  Mobile Phone Towers
Agricultural and Livestock Care
  Water, feeding, evacuation
Retrieve personal items of evacuees
Notes: Be prepared to survey critical infrastructure or support re-entry into critical facilities. Besides performing surveys at the location, consider placing passive dosimeters inside or outside of buildings to determine a dose to an individual occupying that area. Agriculture (especially dairies) will need to continue to operate on a daily basis. Monitoring personnel may need to perform surveys to assist in determining the suitability of areas for the population to re-enter.

## Slide 45: Infrastructure and Re-Entry
Support reentry, cleanup, and mitigation activities
  Support monitoring and decontamination of emergency workers and equipment
  Support monitoring and decontamination efforts for the population
  Support reentry efforts
Temporary entry into a restricted zone under controlled conditions
Notes: Contamination control lines (otherwise known as “hotlines”) are setup to assist personnel exiting the affected areas. While DOE teams will support hotlines (as available) for responders, typically DOE field teams do not provide assistance for population monitoring. Other agencies, like the CDC or Civil Support Teams, are equipped to provide support for population monitoring.

## Slide 46: Contamination Control

## Slide 47: Contamination Control
Keep inside of vehicle as clean as possible
  Use plastic to cover inside of vehicle before deployment
Change PPE often
  Put on clean gloves and shoe covers each time you enter the vehicle
Survey personnel before entering the vehicle
Notes: Prepare the field team vehicle each shift with plastic to protect the vehicle from being contaminated. Field team personnel should survey hands and feet before entering the vehicle. Changing gloves and shoe covers frequently will help control contamination. Place used PPE in a plastic bag for radioactive waste. Place sampling equipment in plastic bags in the vehicle if unable to decontaminate them in the field. After the field team is done for the shift, they should proceed to the hotline. At the hotline, personnel are surveyed as well as equipment and the vehicle, radioactive waste is removed, and the field samples are processed by sample control personnel, and then the plastic sheeting in the vehicle is removed.
If population is sheltered in place, what are PPE requirements of the entry team? Sometimes optics will supersede normal procedure. Instead of wearing a full set of PPE in a neighborhood, could you use just shoe covers and gloves to help ease some of the fears of the sheltered population?

## Slide 48: Contamination Control
Perform personnel and equipment monitoring (contamination check) at beginning and end of shift
Survey vehicle periodically while in the field, document the reading, time, and location
Notes: While in the field, the field team should periodically survey the interior of the vehicle for contamination. When coming back to the clean area, a hotline should be established where surveys of the entire vehicle and personnel are performed.

## Slide 49: Questions?